IREC is unlike most other competitions, since it is not the team with the most powerful rocket that wins. Instead it is the team with the most precise rocket. One great problem we face is climate differences between testing and competition site. A rocket tested to be precise in the cold dense canadian air will not fair well in the light hot air of the desert.

There are many solutions to ensure acurate stoping of the rocket. The most promissing by far is an air braking mechanism which is triggered by an altimeter. With two simple onboard sensors measuring airspeed and altitude a PID controller would have all the information it needs to fire the air brake at an appropriate time.

The next problem is the air brake itself. It must be strong yet lightweight. Common air brakes actuate against the drag force, for example wing spoilers which pop up from the top of the airfoil. However these require large heavy actuators that are acceptable on large aircraft but not high performance rockets. But there is one benifit to the rocket form factor, since rockets tend to fly much faster than air craft a smaller braking surface is required to exhert the same force.

This is what motivates this design for an air brake that actuates perpendicular to the relative airflow. Using this iris configuration limits the size of the braking surface by the diameter of the rocket body. But it allows for lightweight motors and batteries to be used.

The air brake was prototyped using conventional 3d printing teqniques. For the future build a combination of caarbon reinforced 3d printing will be used for the flaps, and a lightweight aircraft grade aluminium can be used for the botom plate. In order to drive the center gear we will use a standard size servo motor controls by a PID loop. By 3d printing the flaps we can inlay material into the structure. Once danger with an air brake is that is one braking surface fails the rocket has uneven drag affect and will result in a loss of control. By 3d printing the flaps we cna inlay a conductive layer of thing copper wire. If a flap breaks off we can detect the loss of continuity and then imediatly retract the remaining flaps limiting the damage to the rocket.

In order to approximate the drag affect of the brakes we use CFD software availible through solidworks to simulate braking at different air speeds. It was imediately noticed that the drag affect of single brake is very small but with multiple brakes in selective positions around the rocket body we can multiple the affect of these brakes. Due to their lightweight we can place multiple brakes without affecting the overall mass of the rocket very much. This is something the depends highly on the geometry of the the final rocket. It is important that we limit vortocies shed by the brake that contact the stabalizing fins. As well brakes should be aft of the CG in order to maintain maximum stability. If brakes are placed forward for the CG we must ensure their moment is less than the moment of the aft brakes. Imaging braking on you bike using only the front brakes...you die.

All together air brakes a a great solutions to the altitude problem but there are still some isues which need to be resolved before this solution can be implemented. There is definately a good benifit from small scale testing before attaching brakes to a high powered rocket traveling in exess of 300 m/s